## Slide 1: Energy Efficient mac protocol
Presented by
S.Jagannathan
MIT,chennai

## Slide 2: What is wireless sensor network
Network of devices that can communicate the information gathered from a monitored field through wireless links.

## Slide 3: Some Applications of Sensor Networks
Data Collection Networks
  Sensing Movement of Glaciers
  Environment Monitoring
Event Triggered Networks
  Military Applications
  Environment Monitoring
    Poisonous gas, pollutants etc.
  National Asset Protection
    Border Patrol,Oil/gas pipelines.

## Slide 4: Evolution
Adaptive Rate Control
CSMA/CD
CSMA/CA
SMAC
TMAC
IEEE 802.11
Carrier Sense Multiple Access with Collision Detection
IEEE 802.3
Carrier Sense Multiple Access with Collision Avoidance
Fixed duty cycle
Adaptive duty cycle
ARC
DMAC/
MMAC
Directional Antennas

## Slide 5: Medium Access Control in Sensor Nets
Important attributes of MAC protocols
  Collision avoidance
  Energy efficiency
  Scalability in node density
  Latency
  Fairness
  Throughput
  Bandwidth utilization
Primary
Secondary

## Slide 6: Reason of Energy Waste
Major sources of energy waste (cont.)
  Idle listening
    Long idle time when no sensing event happens
  Collisions
  Control overhead
  Overhearing
We try to reduce energy consumption from all above sources
Combine benefits of TDMA + contention protocols
Common to all wireless networks
Dominant in sensor nets

## Slide 7: Existing MAC Protocols
Sensor-MAC (S-MAC) : Listen-sleep
Timeout-MAC (T-MAC) : Activation event
WiseMAC : Preamble Sampling

## Slide 8: Sensor-MAC (S-MAC) Design
Tradeoffs
Major components in S-MAC
  Periodic listen and sleep
  Collision avoidance
  Overhearing avoidance
  Massage passing
Latency
Fairness
Energy

## Slide 9: Periodic Listen and Sleep
Problem: Idle listening consumes significant energy
Solution: Periodic listen and sleep
  Turn off radio when sleeping
  Reduce duty cycle to ~ 10% (200ms on/2s off)
sleep
listen
listen
sleep
Latency
Energy

## Slide 10: Periodic Listen and Sleep
Schedules can differ
  Prefer neighboring nodes have same schedule
    — easy broadcast & low control overhead
Node 1
Node 2
sleep
listen
listen
sleep
sleep
listen
listen
sleep
Schedule 2
Schedule 1
1
2

## Slide 11: Overhearing Avoidance
Problem: Receive packets destined to others
Solution: Sleep when neighbors talk
  Basic idea from PAMAS (Singh, Raghavendra 1998)
  But we only use in-channel signaling
Who should sleep?
  All immediate neighbors of sender and receiver
How long to sleep?
  The duration field in each packet informs other nodes the sleep interval

## Slide 12: Message Passing
How to efficiently transmit a long message?
Single packet vs. fragmentations
  Single packet: high cost of retransmission if only a few bits have been corrupted
  Fragmentations: large control overhead (RTS & CTS for each fragment), longer delay
Problem: Sensor network in-network processing requires entire message

## Slide 13: Message Passing
Solution: Don’t interleave different messages
  Long message is fragmented & sent in burst
  RTS/CTS reserve medium for entire message
  Fragment-level error recovery — ACK
  — extend Tx time and re-transmit immediately
Other nodes sleep for whole message time
Fairness
Energy
Msg-level latency

## Slide 14: S-MAC

## Slide 15: Example
Who should sleep when node A is transmitting to B?
All immediate neighbors of both sender & receiver should go to sleep

## Slide 16: Experiment Result
Average source nodes energy consumption
S-MAC consumes much less energy
than 802.11-like protocol w/o sleeping
At heavy load, overhearing avoidance is
the major factor in energy savings
At light load, periodic sleeping plays the key role
0
2
4
6
8
10
200
400
600
800
1000
1200
1400
1600
1800
Average energy consumption in the source nodes
Message inter-arrival period (second)
Energy consumption (mJ)
802.11-like protocol
without sleep
Overhearing
avoidance
S-MAC w/o adaptive listen

## Slide 17: S-MAC Conclusions
Advantages:
  S-MAC offers significant energy efficiency over always-listening MAC protocols.
  S-MAC can function at 10% duty cycle.
Disadvantage
  Sleep and listen periods are predefined and constant which decreases the efficiency of the algorithm under variable traffic load.

## Slide 18: Timeout-MAC (T-MAC) Protocol
Proposed to enhance the poor results of S-MAC protocol under variable traffic load.
Listen period ends when no activation event has occurred for a time threshold TA.
Reduce idle listening by transmitting all messages in bursts of variable length, and sleeping between bursts.
times out on hearing nothing.

## Slide 19: S-MAC Vs T-MAC